## Slide 1: Assembly and Bomb Lab
15-213: Introduction to Computer Systems Recitation 4: Monday, Sept. 16, 2013
Marjorie Carlson Section A

## Slide 2: 回顾：Turning C into Object Code
text
text
binary
binary
Compiler (gcc –Og -S)
Assembler (gcc or as)
Linker (gcc or ld)
C program (p1.c p2.c)
Asm program (p1.s p2.s)
Object program (p1.o p2.o)
Executable program (p)
Static libraries (.a)
  Code in files p1.c p2.c
  Compile with command: gcc –Og p1.c p2.c -o p
    Use basic optimizations (-Og) [New to recent versions of GCC]
    Put resulting binary in file p

## Slide 3: Compiling Into Assembly
C Code (sum.c)
long plus(long x, long y);
void sumstore(long x, long y,
long *dest)
{
long t = plus(x, y);
*dest = t;
}
Generated x86-64 Assembly
sumstore:
pushq %rbx
movq %rdx, %rbx
call plus
movq %rax, (%rbx)
popq %rbx
ret
Obtain (on shark machine) with command
  gcc –Og –S sum.c
Produces file sum.s
Warning: Will get very different results on non-Shark machines (Andrew Linux, Mac OS-X, …) due to different versions of gcc and different compiler settings.

## Slide 4: What it really looks like
.globl sumstore
.type sumstore, @function
sumstore:
.LFB35:
.cfi_startproc
pushq %rbx
.cfi_def_cfa_offset 16
.cfi_offset 3, -16
movq %rdx, %rbx
call plus
movq %rax, (%rbx)
popq %rbx
.cfi_def_cfa_offset 8
ret
.cfi_endproc
.LFE35:
.size sumstore, .-sumstore

## Slide 5: What it really looks like
.globl sumstore
.type sumstore, @function
sumstore:
.LFB35:
.cfi_startproc
pushq %rbx
.cfi_def_cfa_offset 16
.cfi_offset 3, -16
movq %rdx, %rbx
call plus
movq %rax, (%rbx)
popq %rbx
.cfi_def_cfa_offset 8
ret
.cfi_endproc
.LFE35:
.size sumstore, .-sumstore
Things that look weird and are preceded by a ‘.’ are generally directives.
sumstore:
pushq %rbx
movq %rdx, %rbx
call plus
movq %rax, (%rbx)
popq %rbx
ret

## Slide 6: Object Code
Code for sumstore
0x0400595:
0x53
0x48
0x89
0xd3
0xe8
0xf2
0xff
0xff
0xff
0x48
0x89
0x03
0x5b
0xc3
Assembler
  Translates .s into .o
  Binary encoding of each instruction
  Nearly-complete image of executable code
  Missing linkages between code in different files
Linker
  Resolves references between files
  Combines with static run-time libraries
    E.g., code for malloc, printf
  Some libraries are dynamically linked
    Linking occurs when program begins execution
  Total of 14 bytes
  Each instruction 1, 3, or 5 bytes
  Starts at address 0x0400595

## Slide 7: Machine Instruction Example
C Code
  Store value t where designated by dest
Assembly
  Move 8-byte value to memory
    Quad words in x86-64 parlance
  Operands:
    t: Register %rax
    dest: Register %rbx
    *dest: Memory M[%rbx]
Object Code
  3-byte instruction
  Stored at address 0x40059e
*dest = t;
movq %rax, (%rbx)
0x40059e: 48 89 03

## Slide 8: Disassembling Object Code
Disassembled
Disassembler
  objdump –d sum
  Useful tool for examining object code
  Analyzes bit pattern of series of instructions
  Produces approximate rendition of assembly code
  Can be run on either a.out (complete executable) or .o file
0000000000400595 <sumstore>:
400595: 53 push %rbx
400596: 48 89 d3 mov %rdx,%rbx
400599: e8 f2 ff ff ff callq 400590 <plus>
40059e: 48 89 03 mov %rax,(%rbx)
4005a1: 5b pop %rbx
4005a2: c3 retq

## Slide 9
GCC使用举例
两个源程序文件test1.c和test2.c，最终生成可执行文件为test
  gcc -O1 test1.c test2.c -o test
选项-O1表示一级优化，-O2为二级优化，选项-o指出输出文件名
目标文件可用“objdump -d test.o” 反汇编为汇编语言程序
add:
pushl %ebp
movl %esp, %ebp
subl $16, %esp
movl 12(%ebp), %eax
movl 8(%ebp), %edx
leal (%edx, %eax), %eax
movl %eax, -4(%ebp)
movl -4(%ebp), %eax
leave
ret
00000000 <add>:
0: 55 push %ebp
1: 89 e5 mov %esp, %ebp
3: 83 ec 10 sub $0x10, %esp
6: 8b 45 0c mov 0xc(%ebp), %eax
9: 8b 55 08 mov 0x8(%ebp), %edx
c: 8d 04 02 lea (%edx,%eax,1), %eax
f: 89 45 fc mov %eax, -0x4(%ebp)
12: 8b 45 fc mov -0x4(%ebp), %eax
15: c9 leave
16: c3 ret
gcc -E test.c -o test.i
gcc -S test.i -o test.s
gcc –S test.c –o test.s
test.s
位移量
机器指令
汇编指令
编译得到的与反汇编得到的汇编指令形式稍有差异

## Slide 10
两种目标文件
“objdump -d test” 结果
00000000 <add>:
0: 55 push %ebp
1: 89 e5 mov %esp, %ebp
3: 83 ec 10 sub $0x10, %esp
6: 8b 45 0c mov 0xc(%ebp), %eax
9: 8b 55 08 mov 0x8(%ebp), %edx
c: 8d 04 02 lea (%edx,%eax,1), %eax
f: 89 45 fc mov %eax, -0x4(%ebp)
12: 8b 45 fc mov -0x4(%ebp), %eax
15: c9 leave
16: c3 ret
test.o中的代码从地址0开始，test中的代码从80483d4开始！
080483d4 <add>:
80483d4: 55 push ...
80483d5: 89 e5 …
80483d7: 83 ec 10 …
80483da: 8b 45 0c …
80483dd: 8b 55 08 …
80483e0: 8d 04 02 …
80483e3: 89 45 fc …
80483e6: 8b 45 fc …
80483e9: c9 …
80483ea: c3 ret
“objdump -d test.o”结果
test.o：可重定位目标文件
test：可执行目标文件

## Slide 11: Alternate Disassembly
Disassembled
Dump of assembler code for function sumstore:
0x0000000000400595 <+0>: push %rbx
0x0000000000400596 <+1>: mov %rdx,%rbx
0x0000000000400599 <+4>: callq 0x400590 <plus>
0x000000000040059e <+9>: mov %rax,(%rbx)
0x00000000004005a1 <+12>:pop %rbx
0x00000000004005a2 <+13>:retq
Within gdb Debugger
  Disassemble procedure
  gdb sum
  disassemble sumstore

## Slide 12: Alternate Disassembly
Disassembled
Dump of assembler code for function sumstore:
0x0000000000400595 <+0>: push %rbx
0x0000000000400596 <+1>: mov %rdx,%rbx
0x0000000000400599 <+4>: callq 0x400590 <plus>
0x000000000040059e <+9>: mov %rax,(%rbx)
0x00000000004005a1 <+12>:pop %rbx
0x00000000004005a2 <+13>:retq
Within gdb Debugger
  Disassemble procedure
  gdb sum
  disassemble sumstore
  Examine the 14 bytes starting at sumstore
  x/14xb sumstore
Object Code
0x0400595:
0x53
0x48
0x89
0xd3
0xe8
0xf2
0xff
0xff
0xff
0x48
0x89
0x03
0x5b
0xc3

## Slide 13: What Can be Disassembled?
Anything that can be interpreted as executable code
Disassembler examines bytes and reconstructs assembly source
% objdump -d WINWORD.EXE
WINWORD.EXE: file format pei-i386
No symbols in "WINWORD.EXE".
Disassembly of section .text:
30001000 <.text>:
30001000: 55 push %ebp
30001001: 8b ec mov %esp,%ebp
30001003: 6a ff push $0xffffffff
30001005: 68 90 10 00 30 push $0x30001090
3000100a: 68 91 dc 4c 30 push $0x304cdc91
Reverse engineering forbidden by
Microsoft End User License Agreement

## Slide 14: Agenda
Overview of Bomb Lab
Assembly Refresher
Intro to GDB
Unix Refresher

## Slide 15: Bomb Lab
Oh no! Dr. Evil has written an evil program that will “explode” the Shark machines!
The program is in phases, each of which reads in input – something like a password – from standard input.
If your input is correct, you go on to the next phase.
If not, the bomb explodes. The program prints “BOOM!!!” and terminates, and you lose half a point. (Your score is updated automatically – you don’t have to upload anything to Autolab.)

## Slide 16: Bomb Lab
We give you:
  Partial source code, in which Dr. Evil mocks you
  The executable file itself
You can’t read the C source code. So how can you figure out what the program does?
From the binary executable!

## Slide 17: Agenda
Overview of Bomb Lab
Assembly Refresher
Intro to GDB
Unix Refresher

## Slide 18: x86-64 Integer Registers
%rsp
%eax
%ebx
%ecx
%edx
%esi
%edi
%esp
%ebp
%r8d
%r9d
%r10d
%r11d
%r12d
%r13d
%r14d
%r15d
%r8
%r9
%r10
%r11
%r12
%r13
%r14
%r15
%rax
%rbx
%rcx
%rdx
%rsi
%rdi
%rbp
arg 1
arg 2
arg 3
arg 4
arg 5
arg 6
return

## Slide 19: Assembly: Operands
Data type | Syntax | Examples | Notes
Immediate values (constant integers) | Start with $ | $0x0 $-15213 | Don’t forget 0x means hex!
Registers | Start with % | %esi %rax | Can represent a value or an address
Memory locations | Parentheses around a register, or addressing mode – D(Rb,Ri,S) | (%esi) 0x8(%rax) (%rax, %rsi, 4) | Parentheses dereference. If %esi stores an address, (%esi) is the value at that address.

## Slide 20: Assembly: Some Common Operations
Instruction | Effect
mov %rdi, %rax | rax = rdi
add %rdi, %rax | rax = rax + rdi
sub %rdi, %rax | rax = rax - rdi
lea (%rdi, %rsi, 2), %rax | rax = rdi + (2 * rsi) (doesn’t dereference)
call foo | Calls function “foo”
push %eax | Pushes eax onto the stack
pop %eax | Pops a value off the stack and into eax
ret | Returns to the return address (i.e., the next line in the calling function)
nop | Does nothing!
You may see suffixes on the end: b, w, l, q | Specify operand is 1, 2, 4, 8 bytes

## Slide 21: Assembly: Comparisons and Jumps
Remember from class that Assembly uses comparisons and jumps (gotos) to execute various conditionals and loops.
cmp b, a sets the same flags as computing a – b.
test b, a sets the same flags as computing a & b.
These are usually followed by a conditional jump instruction that relies on the results.
Watch out for operand order: cmpl %eax, %edx if %edx > %eax, jg 401095 jump to 401095

## Slide 22: Assembly: Comparisons and Jumps
Instruction | Effect | Instruction | Effect
jmp | Always jump | ja | Jump if above (unsigned >)
je/jz | Jump if =/0 | jae | Jump if above or equal
jne/jnz | Jump if ≠/0 | jb | Jump if below (unsigned <)
jg | Jump if > | jbe | Jump if below or equal
jge | Jump if >= | js | Jump if negative
jl | Jump if < | jns | Jump if nonnegative
jle | Jump if <= |  | 

## Slide 23: Assembly: Comparisons and Jumps
cmp $0x42, %edi
je 400d3b if ____________, jump to 400d3b
cmp %esi, %edx jle 400e71 if_____________, jump to 400e71
test %rdi, %rdi jne 400e87 if ____________, jump to 400e87
edi == 66
edx <= esi
%rdi != 0

## Slide 24: Agenda
Overview of Bomb Lab
Assembly Refresher
Intro to GDB
Unix Refresher

## Slide 25: Your Defusing Toolkit
objdump –t bomb prints the symbol table
strings bomb prints all printable strings
objdump –d bomb prints the Assembly
gdb bomb shows you the executable file in Assembly and lets you step through it line by line, peeking into the registers and stack as you go

## Slide 26: GDB: Stepping Through Code
break <location>
  sets a breakpoint. Location can be a function name or an address.
  Pro tip: you have to reset your break points when you restart GDB!
run / run <filename>
  runs the program up till the next breakpoint.
  Pro tip: instead of typing in your inputs each time, you can put them in a text file, one per line, and run that.
disassemble (or disas – but not dis!!!)
  shows you the current function, with an arrow to the next line.
step / stepi / nexti
  step executes one C statement – it doesn’t work for us.
  stepi steps to the next line of Assembly.
  nexti does the same but doesn’t stop in function calls.
  stepi <n> or nexti <n> steps through n lines.

## Slide 27: GDB: Examining Data
info registers
  prints the (hex) contents of every register.
print $<register>
  prints the contents of a register.
  Note the $ – not a %.
  Use /x or /d, to specify hex or decimal: print /d $rax.
x $<register> / x 0x<address>
  prints what the register points to (or what’s at the given address).
  By default, prints one word (a “word” here is 4 bytes).
  However, in addition to specifying format (now including /s, string), you can specify how many objects of what size to print, in the format x /[num][size][format], for example: x /4wd $rsp

## Slide 28: One Last Hint: sscanf
The bomb frequently calls sscanf to read in formatted arguments.
If you’re not familiar with the formatting used by printf, now’s the time!
Example: %s %x %s represents an input of a string, hex number, and string.
This could be handy in figuring out what kinds of arguments a phase is expecting.
man sscanf!

## Slide 29: Resources
Assignment writeup
GDB cheat sheet: http://csapp.cs.cmu.edu/public/docs/gdbnotes-x86-64.pdf.
CS:APP Chapter 3
If you’re stuck, check the course FAQ: http://www.cs.cmu.edu/~213/faq.html
If that doesn’t help, email us: 15-213-staff@cs.cmu.edu
Office hours: Sun-Thu, 5:30-8:30 pm, in Wean 5207
Peer tutoring: Tue 8:30-11, Mudge Reading Room
Note: if you Google Assembly instructions, make sure what you find is in AT&T syntax, not Intel. (The operands are reversed.)

## Slide 30: Agenda
Overview of Bomb Lab
Assembly Refresher
Intro to GDB
Unix Refresher

## Slide 31: Unix Refresher
At the very least, you should be comfortable with:
  man to read manual pages
  cd to change directories
  ls to list contents of the current directory
  ls –l to list contents with extra info, including permission bits
  scp to send files between your computer and the Shark machines
  ssh to log into the Shark machines
  tar to tar (-cvf) and untar (-xvf) things (-z for optional gzip)
  chmod to change permission bits if necessary
  flags (e.g. –R to apply a command recursively to a folder)
Helpful hints: Tab autocompletes. An up arrow scrolls up through your last few commands.

## Slide 32: Agenda
Overview of Bomb Lab
Assembly Refresher
Intro to GDB
Unix Refresher

## Slide 33: 高阶实验
本课程是“北邮-华为智能基座联合课程”，其目的是介绍华为的鲲鹏处理器（基于ARM v8架构）和openEuler操作系统等。
  到目前为止，大家已初步了解C程序与x86-64机器指令间的映射关系，lab2实验就是让同学们从可执行程序入手，采用逆向工程的手段分析机器指令，推断出程序的功能。
  本学期，我们将增加鲲鹏处理器的内容，同时开设高阶lab2实验，与lab2不同的是可执行程序是在鲲鹏处理器上运行的，换句话说你需要熟悉ARM AArch64的指令才能完成。
  通常情况下，如果熟悉了一种处理器的指令后，再学习其他处理器的指令会非常快。现在我们希望对ARM处理器有兴趣、有探索精神、有好奇心、或自学能力强的同学踊跃报名参加高阶lba2实验。

## Slide 34: 高阶实验
我们提供：
  1、相关的资料和文档
  2、华为鲲鹏计算平台的账号
  3、完成实验后，自动记分牌的分数与普通lab2得的分数等值，但作为鼓励，在“计算机系统基础”课平时成绩+5分（暂定标准）
  注：1.你可以只完成高阶lab2实验，也可以先完成lab2，再尝试完成高阶lab2实验，计入最好成绩。
  注：2.lab2为期2周；高阶lab2为期3周
稍后助教会发出报名的电子文档。